## Slide 1
Computer Networking: A Top Down Approach
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016
Chapter 4 Network Layer:
The Data Plane
These slides have been adapted from the Pearson slides and Prof Rexford @ Princeton.

## Slide 2
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 3: Chapter 4: network layer
chapter goals:
understand principles behind network layer services, focusing on data plane:
  network layer service models
  forwarding versus routing
  how a router works
  generalized forwarding
instantiation, implementation in the Internet

## Slide 4: Network layer
transport segment from sending to receiving host
on sending side encapsulates segments into datagrams
on receiving side, delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 5: Protocol Layers: Host vs Router
5
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 6: Protocol Layers: Encapsulation
Ethernet
IP
TCP
HTTP
HTTP Body

## Slide 7: Two key network-layer functions
network-layer functions:
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to destination
  routing algorithms
analogy: taking a trip
forwarding: process of getting through single interchange
routing: process of planning trip from source to destination

## Slide 8: Network layer: data plane, control plane
Data plane
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
forwarding function
Control plane – Routing
network-wide logic
determines how datagram is routed among routers along end-end path from source host to destination host
accomplished by routing algorithms implemented in routers
Control plane – Network Layer
Internet Control Management Protocol (ICMP)

## Slide 9
Per-router data and control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact in the control plane
Individual router forwards from input port to output port
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 10: Routing versus Forwarding
Routing
  Responsible for finding path(s) to destination host
  Routing algorithm populates a routing table
  Instantiates the forwarding table
Forwarding
  Router consults the forwarding table
  Examines network prefix of destination IP address in IP header
  Uses forwarding table to determine outgoing link
Destination Address | Output Interface
128.96.0.0/16 | 0
128.96.3.0/24 | 1
192.168.0.0/16 | 2

## Slide 11: Network service model
Q: What service model for “channel” transporting datagrams from sender to receiver?
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing

## Slide 12: Datagram Networks
Packet carries Destination Address
No setup; routers maintain no state information
Routers:
  Use the destination address to forward the packet
  Forwarding table maps destination address to output link

## Slide 13: Network layer service models
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?

## Slide 14: Best-effort Service
Best-effort delivery
  Packets may be lost
  Packets may be corrupted
  Packets may be delivered out of order
14
source
destination
IP network

## Slide 15: Best-effort: Simplicity
Never having to say you’re sorry…
  Don’t reserve bandwidth and memory
  Don’t do error detection and correction
  Don’t remember from one packet to next
Easier to survive failures
  Transient disruptions are okay during failover
Easier to support on many kinds of links
  Important for interconnecting different networks

## Slide 16: Best-Effort: Good Enough?
Packet loss and delay
  Sender can resend
Packet corruption
  Receiver can detect, and sender can resend
Out-of-order delivery
  Receiver can put the data back in order
Packets follow different paths
  Doesn’t matter
Network failure
  Drop the packet
Network congestion
  Drop the packet

## Slide 17
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 18: Hierarchical Addressing in U.S. Mail
Addressing in the U.S. mail
  Zip code: 08540
  Building: 35 Olden Street
  Room in building: 306
  Name of occupant: Jennifer Rexford
Forwarding the U.S. mail
  Deliver to the post office in the zip code
  Assign to mailman covering the building
  Drop letter into mailbox for building/room
  Give letter to the appropriate person
???

## Slide 19: IP Addressing
IP addresses are 32 bits expressed in dotted decimal notation
  Example: www.njit.edu 128.235.251.25
Each network interface has an IP Address
  Hosts may have more than one interface and hence IP address e.g. Ethernet and WiFi
  Routers have one IP address per interface
10000000
111010111
11111011
00011011
128
235
251
25

## Slide 20: IP Addressing: Route Aggregation
IP addresses are 32 bits = 232 addresses
  We can’t have a forwarding table with 232 entries (4,294,967,296) entries!
  IP addresses cannot be assigned randomly
IP addresses are structured hierarchically
  Assign groups of addresses to an organization
  Example: NJIT allocated 128.35.0.0/16
  High-order 16 bits indicates NJIT
  Low-order 16 bits managed by NJIT (and may be structured into further levels of hierarchy)
Route aggregation: One prefix used by ISP to route to all networks and machines at NJIT

## Slide 21: Scalability Challenge
Suppose hosts had arbitrary addresses
  Then every router would need a lot of information
  …to know how to direct packets toward every host
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
5.6.7.8
2.4.6.8
1.2.3.5
5.6.7.9
2.4.6.9
1.2.3.4
1.2.3.5
forwarding table

## Slide 22: Subnet Mask or Prefix
Subnet mask or Prefix
  A bit mask with 1’s in the network number position
  Address & netmask strips away host bits
  Different length prefixes or masks may be used at different levels of routing hierarchy
For NJIT, the subnet mask is 16
11111111
111111111
00000000
00000000
16 bits - network
16 bits - host

## Slide 23: Subnet Mask or Prefix (cont)
Many organizations have multiple internal networks and allocate IP addresses accordingly
Example: afsaccess1.njit.edu, the subnet mask is 25 bits
Eth1: Link encap:Ethernet HWaddr 00:50:56:B4:47:FF inet addr:128.235.208.201 Mask:255.255.255.128
11111111
111111111
11111111
10000000
25 bits - network
7 bits - host

## Slide 24: Scalability Improved
Number related hosts from a common subnet
  1.2.3.0/24 on the left LAN
  5.6.7.0/24 on the right LAN
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 25: Easy to Add New Hosts
No need to update the routers
  E.g., adding a new host 5.6.7.213 on the right
  Doesn’t require adding a new forwarding-table entry
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table
host
5.6.7.213

## Slide 26: Special IP Addresses
Special IP Addresses | Description
0.0.0.0 | “this host”. Rarely used.
Network = 0, Host | Host on “this” network
255.255.255.255 | Local Broadcast
Network, Host = all one’s Example: 128.235.208.255 | Directed Broadcast
127.0.0.1 | Loopback address
General Rule: All zeroes means “this”; all one’s means “all”

## Slide 27: IP addressing: Hosts and Routers
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 28: Subnets
IP address:
  subnet part - high order bits
  host part - low order bits
what’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
223.1.2.0/24
223.1.3.0/24
223.1.1.0/24

## Slide 29: Subnets
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
Subnet mask 24 bits

## Slide 30: IP Addressing: Hierarchical Structure
Network ID
SubNet ID
Host ID
“Public” Network Mask(x bits)
“Site” Subnet Mask (y bits)
Host Mask (32 bits)
0
x
y
31
Assigned to Site
Allocated by Site
Allocated by Site

## Slide 31: IP Addressing: Hierarchical Structure Example: 223.1.0.0/24
Network ID
SubNet ID
Host ID
“Public” Network Mask(16 bits)
“Site” Subnet Mask (24 bits)
Host Mask (32 bits)
0
16
24
31
Assigned to Site
Allocated by Site
Allocated by Site
Subnet | Prefix
0 | 223.1.0.0/24
1 | 223.1.1.0/24
2 | 223.1.2.0/24
3 | 223.1.3.0/24
… | …
255 | 223/1.255.24

## Slide 32: IP Addressing: Hierarchical Structure Example: Site = 192.168.42.0/24
Network ID
SubNet ID
Host ID
“Public” Network Mask(24 bits)
“Site” Subnet Mask (27 bits)
Host Mask (32 bits)
0
24
27
31
Assigned to Site
Allocated by Site
Allocated by Site
Subnet | Prefix
0 | 192.168.42.0/27
1 | 192.168.42.32/27
2 | 192.168.42.64/27
3 | 192.168.42.128/27
… | …
7 | 192.168.42.224/27

## Slide 33: IP Addressing: Hierarchical Structure Example: 128.235.0.0/16
Network ID
SubNet ID
Host ID
“Public” Network Mask(16 bits)
“Site” Subnet Mask (25 bits)
Host Mask (32 bits)
0
16
25
31
Assigned to Site
Allocated by Site
Allocated by Site
Subnet | Prefix
0 | 128.235.0.0/25
1 | 128.235.0.128/25
2 | 128.235.1.0/25
3 | 128.235.1.128/25
… | …
512 | 128.236.255.128/25

## Slide 34: Address Allocation
IANA
AfriNIC
APNIC
ARIN
LACNIC
RIPE
http://www.iana.org/assignments/ipv4-address-space
Allocate blocks to Tier 1 ISPs and Large Organizations
Allocate sub-blocks to Tier2 SPs
Your computer
or Gateway
Prefixes
Increase
with
depth
of
hierarchy

## Slide 35: IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 36: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing
information:

## Slide 37: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 38: IP addressing: the last word...
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers http://www.icann.org/
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 39: History of IP Address Allocation

## Slide 40: Classful Addressing
In the olden days, only fixed allocation sizes
  Class A: 0*
    Very large /8 blocks (e.g., MIT has 18.0.0.0/8)
  Class B: 10*
    Large /16 blocks (e.g,. NJIT has 128.235.0.0/16)
  Class C: 110*
    Small /24 blocks (e.g., AT&T Labs has 192.20.225.0/24)
  Class D: 1110* for multicast groups
  Class E: 11110* reserved for future use
This is why folks use dotted-quad notation!

## Slide 41: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 42: Classless Inter-Domain Routing (CIDR)
IP Address : 12.4.0.0 IP Mask: 255.254.0.0
00001100
00000100
00000000
00000000
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network.
Network number = IP address + Mask
Written as 12.4.0.0/15

## Slide 43: Hierarchical Address Allocation
Hierarchy is key to scalability
  Address allocated in contiguous chunks (prefixes)
  Today, the Internet has about 400,000 prefixes
12.0.0.0/8
12.0.0.0/16
12.254.0.0/16
12.1.0.0/16
12.2.0.0/16
12.3.0.0/16
:
:
:
12.3.0.0/24
12.3.1.0/24
:
:
12.3.254.0/24
12.253.0.0/19
12.253.32.0/19
12.253.160.0/19
:
:
:
:
:

## Slide 44: Obtaining a Block of Addresses
Internet Corporation for Assigned Names and Numbers (ICANN)
  Allocates large blocks to Regional Internet Registries
Regional Internet Registries (RIRs)
  E.g., ARIN (American Registry for Internet Numbers)
  Allocates to ISPs and large institutions
Internet Service Providers (ISPs)
  Allocate address blocks to their customers
  Who may, in turn, allocate to their customers…

## Slide 45: Pre-CIDR (1988-1994): Steep Growth
Growth faster than improvements in equipment capability

## Slide 46: CIDR (1994-1996): Much Flatter
Efforts to aggregate

## Slide 47: CIDR Growth (1996-1998): Roughly Linear
Good use of aggregation, and peer pressure!

## Slide 48: DotCom Boom (1998-2001): Steep Growth
Internet boom and increased multi-homing

## Slide 49: Long Term (1989-2005): Post-Boom
Today we are up to ~400,000 prefixes

## Slide 50
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 51: Router architecture overview
high-seed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operttes in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame
high-level view of generic router architecture:

## Slide 52: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 5
switch
fabric

## Slide 53: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based on any set of header field values
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 5
switch
fabric

## Slide 54: Longest prefix matching
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix matching
Link interface
0
1
2
3

## Slide 55: Input port queuing
fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric

## Slide 56: Output ports
buffering required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
Datagram (packets) can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality

## Slide 57: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric

## Slide 58: How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gpbs link: 2.5 Gbit buffer
recent recommendation: with N flows, buffering equal to
RTT C
.
N

## Slide 59: Scheduling mechanisms
scheduling: choose next packet to send on link
FIFO (first in first out) scheduling: send in order of arrival to queue
  real-world example?
  discard policy: if packet arrives to full queue: who to discard?
    tail drop: drop arriving packet
    priority: drop/remove on priority basis
    random: drop/remove randomly
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)

## Slide 60: Scheduling policies: priority
priority scheduling: send highest priority queued packet
multiple classes, with different priorities
  class may depend on marking or other header info, e.g. IP source/dest, port numbers, etc.
  real world example?
high priority queue
(waiting area)
low priority queue
(waiting area)
arrivals
classify
departures
link
(server)
1
3
2
4
5
5
5
2
2
1
1
3
3
4
4
arrivals
departures
packet in service

## Slide 61: Scheduling policies: still more
Weighted Fair Queuing (WFQ):
generalized Round Robin
each class gets weighted amount of service in each cycle
real-world example?

## Slide 62
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 63: The Internet network layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 64: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 65: IP fragmentation, reassembly
network links have MTU (max.transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 66: IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 67: IP addresses: how to get one?
Q: How does a host get IP address?
Static: hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
Dynamic:
  DHCP: Dynamic Host Configuration Protocol: dynamically get address from a server
  “plug-and-play”

## Slide 68: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network (more shortly)
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 69: DHCP Message Format
0
31
16
8
24
OP
HTYPE
HLEN
HOPS
Request (1)/
Response (2)
Hardware Type
(Ethernet (1)
Hardware Len
(Ethernet (6)
TRANSACTION ID
SECONDS
FLAGS
Match requests and replies
CLIENT IP ADDRESS
Client: 0.0.0.0 when unknown
YOUR IP ADDRESS
SERVER IP ADDRESS
ROUTER IP ADDRESS
Server: IP address assigned to client
CLIENT HARDWARE ADDRESS
Client: MAC address
…
options
Relay Agent: Router IP address

## Slide 70: DHCP Message Format - Options
type
length
value
Options Structure
Option Type | Option Value
53 | Message Code (Discover, Offer, Request, Ack, …)
51 | IP address lease time
1 | Subnet Mask
3 | First-Hop Router(s)
6 | DNS Server(s)

## Slide 71: DHCP client-server scenario (local LAN)
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 72: DHCP client-server scenario (local LAN)
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 73: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS server
  network mask (indicating network versus host portion of address)

## Slide 74: DHCP: example
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP Server Not on Local LAN:
Relay Agent on Local Router ”relays” DHCP requests and responses between DHCP client and server

## Slide 75: DHCP: example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router

## Slide 76: DHCP: Wireshark output (home LAN)
Message type: Boot Reply (2)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK
Option: (t=54,l=4) Server Identifier = 192.168.1.1
Option: (t=1,l=4) Subnet Mask = 255.255.255.0
Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092;
IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
reply
Message type: Boot Request (1)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A;
Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101
Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name
3 = Router; 6 = Domain Name Server
44 = NetBIOS over TCP/IP Name Server
……
request

## Slide 77: Network Layer – Control Plane
Section 5.6 Kurose & Ross 7th Ed

## Slide 78: ICMP: internet control message protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams (protocol 1)
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 79: ICMP Messages
0
31
16
8
24
Type
Echo Request (8)/
Echo Reply (0)
Code
Reason Code
Checksum
Identifier
Sequence #
0
31
16
8
24
Type
Code
Checksum
Unused
Echo Request/Reply Message Format (ping)
Optional Data (echoed in response)
Destination Unreachable (Router return to host on error):
IP Header + first 64 bytes of datagram
Packet that caused error
Destination
Unreachable (3)
Reason (0-12)
Used in matching
Request & Reply
e.g. incremented on each new request
Used in matching
Request & Reply
Used in matching
Request & Reply
e.g. mimic “port:”

## Slide 80: Traceroute and ICMP
source sends series of UDP segments to destination
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number
when datagram in nth set arrives to nth router:
  router discards datagram and sends source ICMP message (type 11, code 0)
when ICMP message arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes

## Slide 81: Traceroute Variations and Issues
Variations:
Uses UDP with increasing UDP port numbers
  Start at high value to minimize possibility that real application using port
  Increment on each request to match requests and replies
  Original implementation by Van Jacobson
Uses ICMP Echo Request
  Uses Identifier and Sequence Number to match requests and replies
Uses TCP SYN to well-known port
  To get around firewalls
Issues:
Each probe may travel a different path
Requests and Responses may travel different paths
UDP messages with unknown port numbers and ICMP messages may be blocked