## Slide 1: Recap
Adapted from Kurose & Ross textbook, J. Rexford @ Princeton slides

## Slide 2: Key Goals, Key Concepts
Naming and addressing
  DNS names, IP address, Link-layer addresses
  Hierarchy
Reliability
  Reliable data transfer
    At most once semantics: Sequence numbers and Duplicate Detection
    Random, exponential back-off on retransmissions
  Stateful vs Stateless, Hard State versus Soft State
  Idempotence
Scaling and Performance
  Hierarchy
  Caching
  Stateful vs Stateless, Hard State versus Soft State
Distributed Management
  Hierarchy
Modularity
  Protocol Layering: Well-defined Interface and hiding implementation internals
  Encapsulation and Decapsulation at each layer of the protocol stack

## Slide 3: Application Design
Client-Server, Peer-to-Peer
  Client-Server: HTTP, DNS, DHCP, video streaming
  Peer-to-Peer: Routing Protocols
State (across messages)
  Server maintains no (dynamic) state about client
  Protocol messaging strives to be self-contained where possible
  State used as an optimization; easily recoverable; soft state
At most once semantics
  Design messages to be idempotent (to deal with server crashes, network failures)
Persistent Transport Layer Connections (TCP)
  E.g. SMTP, HTTP1.1
Extensible
  Version numbers
  Self-describing data format e.g. DHCP type-value pairs, DNS RRs, HTTP header fields
Secure
Manageable

## Slide 4: Design Principles
End-to-End Argument
  The application knows best
    Perform functionality at the end-systems or at the application layer since application knows best what it needs. Do not bury at lower layer – may get it wrong and may not provide an end-to-end guarantee
  Example: If a file server application needs to detect errors on a file transfer over a network, is there a point in the link layer doing it?
    Not for correctness. The application will need to do it (again) anyway.
    Maybe, for performance reasons

## Slide 5: Hierarchy
Scalability of large systems
  Cannot store all information everywhere
  Cannot centrally coordinate everything
Hierarchy to manage scale
  Divide system into smaller pieces
Hierarchy to divide control
  Decentralized management
Examples in the Internet
  IP addresses, routing protocols, DNS, Content Distribution Networks

## Slide 6: Hierarchy: IP Address Blocks
Number related hosts from a common subnet
  1.2.3.0/24 on the left LAN
  5.6.7.0/24 on the right LAN
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 7: Hierarchy: IP Address Blocks
Separation of control
  Prefix: assigned to an institution
  Addresses: assigned by institution to its nodes
Who assigns prefixes?
  Internet Corporation for Assigned Names & Numbers
  Regional Internet Registries (RIRs)
  Internet Service Providers (ISPs)
  Stub networks
  Regions within an enterprise

## Slide 8: Hierarchy: Routing Protocols
AS-level topology
  Nodes are Autonomous Systems (ASes)
  Edges are links and business relationships
  Hides the detail within each AS’s network
1
2
3
4
5
6
7
Client
Web server

## Slide 9: Hierarchy: Domain Name System
com
edu
org
ac
uk
zw
arpa
root
bar
west
east
foo
my
ac
cam
usr
in-
addr
12
34
56
generic domains
country domains
my.east.bar.edu
usr.cam.ac.uk
12.34.56.0/24

## Slide 10: Naming and Addressing
Host name to IP address
  Mnemonic names to location-dependent addresses
  E.g., from www.cnn.com to 64.236.16.20
  Using the Domain Name System (DNS)
From IP address to MAC address
  From hierarchical global address to interface card
  E.g., from 64.236.16.20 to 00-15-C5-49-04-A9
  Using the Address Resolution Protocol (ARP)

## Slide 11: Identifiers versus Locators: Mobile IP
wide area network
home
network
visited
network
3
2
4
1
correspondent addresses packets using home address of mobile
home agent intercepts packets, forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 12: Caching
Duplicating data stored elsewhere
  To reduce latency for accessing the data
  To reduce resources consumed
Caching is often quite effective
  Speed difference between cache and primary copy
  Locality of reference, and small set of popular data
Examples from the Internet
  DNS caching, Web caching
But need a mechanism to detect stale data (aka cache consistency)
  DNS TTL, HTTP Conditional GET

## Slide 13: Caching: DNS Caching
Application
DNS resolver
Local DNS
server
1
10
DNS cache
DNS query
DNS response
2
9
Root server
Top-level
domain server
Second-level
domain server
3
4
5
6
7
8

## Slide 14: Caching: Web Caching
Caching location
  Proxy cache
  Browser cache
Better performance
  Lower RTT
  Existing connection
  Less network load
client
Proxy
server
client
HTTP request
HTTP request
HTTP response
HTTP response
HTTP request
HTTP response
origin
server
origin
server

## Slide 15: Cache Consistency: Stale Data
Cache consistency is a hard problem
  Ensuring the cached copy is not out of date
Strawman: explicit revocation or updates
  Keep track of everyone who has cached information
  If name-to-host mapping changes, update caches
Soft state solution
  DNS responses include a “time to live” (TTL) field
  Cached entry is deleted after TTL expires

## Slide 16: Reliable Data Transfer: Common Mechanisms
Requirements | Mechanisms
Recovery from packet errors | Checksum (detection) Feedback (ack w/sequence number) Sequence Number (duplicate detection & loss detection)
Recovery from packet loss | Timer in sender – Retransmission on time-out Random, exponential backoff on retries to desynchronize and reduce chance of further packet loss

## Slide 17
Error Detection:
  Checksum: TCP, UDP, IPv4
  CRC: Ethernet, WiFi
Retransmissions: exponential backoff, randomization
  Ethernet, WiFi random access and backoff to avoid collisions
  TCP retransmissions on packet loss and errors
  Applications using UDP such as DHCP/DNS
Feedback: Sequence Numbers and ACKs
  TCP
  WiFi
  Applications using UDP such as DHCP,DNS (called transaction id, message id)
Reliable Data Transfer: Common Mechanisms

## Slide 18: Layering: A Modular Approach
Sub-divide the problem
  Each layer relies on services from layer below
  Each layer exports services to layer above
Interface between layers defines interaction
  Hides implementation details
  Layers can change without disturbing other layers
Link hardware
Host-to-host connectivity
Application-to-application channels
Application

## Slide 19: Layering: Internet Protocol Suite
UDP
TCP
Data Link
Physical
Applications
The Hourglass Model
Waist
The waist facilitates interoperability
SMTP
HTTP
DHCP
DNS
TCP
UDP
IP
NET1
NET2
NETn
…

## Slide 20: Data Plane
Packet Forwarding from source host to destination host

## Slide 21: Encapsulation
User data
application
User data
Application Header
Application data
TCP Header
TCP
Application data
TCP Header
IP Header
Application data
TCP Header
IP Header
Ethernet
Header
Ethernet
Trailer
TCP segment
IP datagram
Ethernet frame
Application message
IP
Ethernet
Driver
Ethernet
Link
Reference: WR Stevens TCP Illustrated Volume 1, Addison-Wesley

## Slide 22: Demultiplexing
Separating multiple streams out of one
  Recognizing the separate streams
  Treating the separate streams accordingly
Examples in the Internet
Frame header
Packet header
TCP header
User
data
type
protocol
port #

## Slide 23: Demultiplexing
application
TCP
IP
Ethernet
Driver
UDP
application
application
application
ICMP
OSPF
ARP
Demux
On port
Demux
On protocol
number
Demux
On frame type
In Ethernet
Header
…
…
Reference: WR Stevens TCP Illustrated Volume 1, Addison-Wesley

## Slide 24: (De)multiplexing: With a NAT
NAT
inside
outside
10.0.0.1
10.0.0.2
138.76.29.7

## Slide 25
Protocol Layers: Host vs Router
4-5
5
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 26: Ethernet Header
Destination MAC address
48 bits
16-bit Upper layer protocol
Demultiplex
Addressing
14 bytes
Source MAC address
Addressing

## Slide 27: IP Header
Version #
Total IP packet length (bytes)
32 bits
16-bit identifier
Header checksum
time to live (TTL)
32 bit source IP address
IP Header
Length (bytes)
Type of service
flags
Fragment offset
Upper layer protocol
32 bit destination IP address
options (if any)
Fragmentation
Reliability
Routing
Demultiplex
Addressing
Addressing
20 bytes

## Slide 28: UDP Header
16-bit source port number
32 bits
Header checksum
Reliability
Demux
8 bytes
16-bit destination port number
16-bit UDP packet length (bytes)
Demux

## Slide 29: TCP Header
32 bits
16-bit window size
32-bit sequence number
flags
options (if any)
Flow Control
20 bytes
16-bit source port number
Demultiplex
16-bit destination port number
Demultiplex
32-bit acknowledgement number
Reliability
Reliability
reserved
Header
length
Header checksum
3-way handshake & close
16-bit urgent pointer
Reliability

## Slide 30: DNS Packet Format
32 bits
Message Identifier
Reliability
Message Type and Flags
# question RRs
# answer RRs
# authoritative RRs
# additional RRs
Variable # of Question RRs
Variable # of Answer RRs
Variable # of Authoritative RRs
Variable # of Additional RRs
DNS Functions
DNS Functions
DNS Functions
DNS Functions
DNS Functions

## Slide 31: DNS Resource Record Format
Name (variable-length) e.g. afsconnect1.google.com, mx1.comcast.net
Class (16 bits)
TTL (32 bits)
Length (16 bits)
Data (variable-length) = answer to query
Type (16 bits) e.g. A, MX, CNAME, NS
Caching

## Slide 32: HTTP Packets: Response
HTTP/1.1 200 OK\r\n
Date: Sun, 26 Sep 2010 20:09:20 GMT\r\n
Server: Apache/2.0.52 (CentOS)\r\n
Last-Modified: Tue, 30 Oct 2007 17:00:02 GMT\r\n
ETag: "17dc6-a5c-bf716880"\r\n
set-cookie: 1678 \r\n
Accept-Ranges: bytes\r\n
Content-Length: 2652\r\n
Keep-Alive: timeout=10, max=100\r\n
Connection: Keep-Alive\r\n
Content-Type: text/html; charset=ISO-8859-1\r\n
\r\n
data data data data data ...
Caching
Persistence
State
Success/Failure Response Code

## Slide 33: Control Plane
Enabling, Controlling Forwarding Plane

## Slide 34: Control Plane Protocols
Network Layer
  Routing Protocols
  ICMP
Network Layer to Link Layer
  ARP --- Resolving IP to Link Layer addresses
Fundamental Infrastructure services
  DHCP --- Network layer configuration
  DNS --- Resolving user-friendly hostname to IP addresses

## Slide 35: ARP protocol: same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 36: ARP Message Format
ARP runs over Link Layer e.g. Ethernet
Hardware Type (Eth = 1)
Protocol Type (IPv4 = 0x800)
Operation (Request/Reply)
HLEN
PLEN
SENDER HA (6 bytes for MAC address)
SENDER IP (4 bytes for IPv4 address)
TARGET IP (4 bytes for IPv4 address)
TARGET HA (6 bytes for MAC address)
Sender fills
own MAC, IP
In request
Sender fills
In target IP
In request
Sender is looking for
target MAC in request
Addressing
Addressing
Addressing
Addressing

## Slide 37: Management Plane
Monitoring, Troubleshooting and Configuring the Dara and Control Planes

## Slide 38: Monitoring and Troubleshooting Tools
Ping
Traceroute
Netflow (did not cover this)

## Slide 39: Traceroute and ICMP
source sends series of UDP segments to destination
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number
when datagram in nth set arrives to nth router:
  router discards datagram and sends source ICMP message (type 11, code 0)
when ICMP message arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes