## Slide 1
Computer Networking: A Top Down Approach
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016
Chapter 5 Network Layer:
The Control Plane
These slides have been adapted from the Pearson slides. S. Thomson 03/2017.

## Slide 2
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 3: Making routing scalable
scale: with billions of destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice

## Slide 4: Internet approach to scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
Collection of routers under common administrative control e.g. ISP, large company
Collection of subnets (routing prefixes => route aggregation)
Present common routing policy to Internet
Identified by an AS number assigned: Internet Assigned Numbers Authority (IANA) -> Reginal Internet Registry (RIR)
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

## Slide 5: ARIN AS Assignment Example

## Slide 6: Internet approach to scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
inter-AS routing
routing among AS’es
gateways perform inter-domain routing (as well as intra-domain routing)
intra-AS routing
routing among hosts, routers in same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocol
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es

## Slide 7: Types of Autonomous Systems
Stub AS
  Carries traffic for which it is source or destination
  Does not route traffic between AS’s
Multi-homed stub AS
  Like a stub AS, but connected to multiple other ASes
Transit AS
  Routes to and from other AS e.g. ISP

## Slide 8: Intra-AS Routing
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First (IS-IS protocol essentially same as OSPF)
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary, Informational RFC published in 2016)

## Slide 9: OSPF (Open Shortest Path First)
IETF standard
uses link-state algorithm
  link state packet dissemination
  topology map at each node
  route computation using Dijkstra’s algorithm
router floods OSPF link-state advertisements to all other routers in entire AS
  carried in OSPF messages directly over IP (rather than TCP or UDP) Protocol number 89
  link state: for each attached link
IS-IS routing protocol: nearly identical to OSPF

## Slide 10: OSPF “advanced” features
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different TOS (e.g., satellite link cost set low for best effort ToS; high for real-time ToS)
integrated uni- and multi-cast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.

## Slide 11: Hierarchical OSPF
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers

## Slide 12: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’es.

## Slide 13
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 14: Inter-AS tasks
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS3
AS2
3b
3c
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
3a

## Slide 15: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy

## Slide 16: BGP Sessions
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
Pairs of routers exchange routing information via BP sessions over semi-permanent TCP connections
  One connection between AS Gateway Routers (eBGP)
  Internally distributed to routers within AS via a mesh of internal BGP sessions (iBGP)

## Slide 17: BGP Sessions
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protocols

## Slide 18: BGP Learns Aggregated Subnet Prefixes
Advertize
200.23.64.0/22” to AS1
200.23.64.0/24
200.23.67.0/24
200.23.66.0/24
AS3
AS1
AS2
“Advertize 200.23.67.0/24” to AS1
200.23.65.0/24
.
.
.
.
.
.
3a
2a
Route
Aggregation
Longest Prefix
Match

## Slide 19: Internet inter-AS routing: BGP
BGP routers send route announcements
  Destination address block/prefix/subnet
  Path of AS numbers the packet will take
  BGP Attributes
Key attributes
  AS-PATH: Sequence of ASs through which advertisement passed
  If a router sees a loop, reject
  Next-Hop: Identifies the router IP address of the AS gateway router that sent the advertisement to this AS
    Intra-AS routing knows how to get to the “next hop” IP address

## Slide 20: BGP basics
when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c:
  AS3 promises to AS2 it will forward datagrams towards prefix X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X

## Slide 21: BGP path advertisement
Based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
Based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c

## Slide 22: Path attributes and BGP routes
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
Policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other other neighboring ASes

## Slide 23: BGP path advertisement
AS1 gateway router 1c learns path AS2,AS3,X from 2a
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
Based on policy, AS1 gateway router 1c chooses path AS3,X, and advertises path within AS1 via iBGP

## Slide 24: BGP: achieving policy via advertisements
A advertises path Aw to B and to C
B chooses not to advertise BAw to C:
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 25: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 26: Updating the Forwarding Table
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations

## Slide 27: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: “path to X goes through 1c”
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
AS3,X
Q: how does router set forwarding table entry to distant prefix?
1
2
1
2
dest
interface
…
…
X
…
…
1
physical link
local link interfaces
at 1a, 1d

## Slide 28: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: “path to X goes through 1c”
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
Q: how does router set forwarding table entry to distant prefix?
dest
interface
…
…
X
…
…
2
1a: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 2
1
2

## Slide 29: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 30: Hot Potato Routing
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS1,AS3,X
OSPF link weights
201
152
112
263

## Slide 31: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its net.
intra-AS: single admin, so no policy decisions needed
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy may dominate over performance